Output power during the half period
Linear functions are boring, let’s curve it like that:
1. f(x) = x
2. …
### Rounding the curve
Let’s start from circle equation
left lbrace binom{x = r sin( %ialpha )}{y = r cos (%ialpha)} right rbrace
Move circle up
left lbrace binom{x = r sin(%ialpha)}{y = r - r cos(%ialpha)} right rbrace, %ialpha in [ %tau/2; %tau/4 ]
Convert into single function (red graph)
stack{sin( %ialpha ) = x/r; # %ialpha = arcsin(x/r) # y = r - r cos(arcsin(x/r)) # cos(%ialpha ) = sqrt{ 1 - sin(%ialpha)^2 } # y = r - r sqrt{ 1 - (x/r)^2 } }
Let’s find the middle part of the curve we’re interested in (intersection with green line)
stack{ y = r - r sqrt{1 - (x/r)^2} intersection y = r - x # r - r sqrt{1 - (x/r)^2} = r - x # x = r sqrt{1 - (x/r)^2} # x = sqrt{ r^2 - x^2 } # x^2 = r^2 - x^2 # 2x^2 = r^2 # x = r/sqrt2 }
Apparently we don’t care about that intersection.
Intersection with y = x – b (yellow line)
stack{ y = r - r sqrt{1 - (x/r)^2} intersection y = x - b # r - r sqrt{1 - (x/r)^2} = x - b # r sqrt{ 1 - (x/r)^2 } = r + b - x # r^2( 1 - (x/r)^2 ) = ( r+b )^2 - 2x( r+b ) + x^2 # r^2 - x^2 = r^2 + 2rb + b^2 - 2xr - 2xb + x^2 # 2x^2 -2xb - 2xr + 2rb + b^2 = 0 # 2x^2 - 2x( r+b ) + (2rb+b^2) = 0 # A = 2; B = -2r - 2b; C = 2rb + b^2 # D = B^2 -4AC = 4( r+b )^2 - 4( 2 times (2rb + b^2) ) = 4r^2 + 8rb + 4b^2 - 16rb -8b^2 # D = 4r^2 - 8rb - 4b^2 # x_1,2 = {-B +-sqrt D}over {2A} # x_1 = { 2r + 2b - sqrt{4r^2 - 8rb - 4b^2} } over 4 = 0.5r + 0.5b - 0.25sqrt{4r^2 - 8rb - 4b^2} # x_2 = { 2r + 2b + sqrt{4r^2 - 8rb - 4b^2} } over 4 = 0.5r + 0.5b + 0.25sqrt{4r^2 - 8rb - 4b^2} }
We need that line to intersect two points at distance exactly 1:
stack { x_2 - x_1 = 1 # 0.5sqrt{4r^2 - 8rb - 4b^2} = 1 # sqrt{4r^2 - 8rb - 4b^2} = 2 # 4r^2 - 8rb - 4b^2 = 4 # 4b^2 + 8rb - 4r^2 + 4 = 0 # A = 4; B = 8r; C = 4 - 4r^2 # D = 64r^2 - 4 times 4 times ( 4 - 4r^2 ) = 64r^2 - 64 + 64r^2 = 128r^2 - 64 # b = {-8r +- sqrt{ 128r^2 - 64 }} over { 8 } = -r +- sqrt{ 2r^2 - 1 } }
stack { x_1 - x_2 = 1 # -0.5sqrt{4r^2 - 8rb - 4b^2} = 1 # sqrt{4r^2 - 8rb - 4b^2} = -2 # 4r^2 - 8rb - 4b^2 = 4 # dotslow }
We need smaller |b| from that, resulting in yellow line y = x – b
b = sqrt{ 2r^2-1 }-r
Now we need first intersection point with our circle (red curve), it will be our new zero: stack{ x_1 = 0.5r + 0.5b - 0.25 sqrt{ 4r^2 - 8rb - 4b^2 } # b = sqrt{ 2r^2 - 1 } - r # x_1 = 1/2r + 1/2 sqrt { 2r^2 - 1 } - 1/2r - 1/4 sqrt{ 4r^2 - 8r sqrt{2r^2 - 1} + 8r^2 - 4(sqrt{2r^2 - 1} - r)^2 } # x_1 = 1/2 sqrt{ r^2 - 1 } - 1/4 sqrt{ 12r^2 - 8r sqrt{2r^2 - 1} - 4(2r^2-1 - 2r sqrt{2r^2 - 1} + r^2) } # x_1 = 1/2 sqrt{ r^2 - 1 } - 1/4 sqrt{ 12r^2 - 8r sqrt{2r^ 2-1} - 8r^2 + 4 + 8r sqrt{2r^2-1} - 4r^2 } # x_1 = 1/2sqrt{ 2r^2 - 1 } - 1/4sqrt{ 4 } = 1/2 sqrt{ 2r^2-1 } - 1/2 }
stack { y_1 = r - r sqrt{ 1 - (x/r)^2 } = r - r sqrt{ 1 - {(1/2 sqrt{2r^2 - 1} - 1/2)^2} over r^2 } # 1/2 sqrt{ 2r^2 - 1 } = sqrt{1/2r^2 - 1/4} # y_1 = r - r sqrt{ 1 - {1/2r^2 - 1/4 - sqrt{1/2r^2 - 1/4} + 1/4} over r^2 } # y_1 = r - r sqrt{ {r^2 - 1/2r^2 + sqrt{1/2r^2 - 1/4}} over r^2 } = r - sqrt{ 1/2r^2 + sqrt{1/2r^2-1/4} } }
Now lets move our circle by those offsets
y = r - r sqrt{ 1 - ((x + x_1)/r)^2 } - y_1

Resources
Graph generator https://www.desmos.com/calculator